Petit retour sur le TD1
Some aspect concerning the LMDZ dynamical core and its use
1. Grid
Staggered grid and dynamics/physics interface
Zooming capability
Vertical discretization
Nudging
2. Temporal scheme and filtering
Temporal schemes illustrated on a 0D model
The Matsuno/Leapfrog scheme
CFL criterion and longitudinal filtering
3. Dissipation
Principle of dissipation in 1D
Operator splitting
Constraints on the time step

---
iim, jjm, llm
Defined at
The compilation
option
-d 64x48x29
In makegcm
Or makelmdz*

---
clat
dzomy *180°
dx=360° /iim
dy=180°/jjm
Zoom center :
clon : longitude (degrees)
clat : latitude (degrees)
grossimx/y : zooming factor
in x/y
Computed as the ration of the
Finest model grid mesh length and of the equivalent length for the regular grid with same number of points.
dzoomx/y : fraction of the grid in which the resolution is increased.
dzomx * 360°
clon
http://lmdz.lmd.jussieu.fr/developpeurs/notes-techniques

---
Zoom center :
clon : longitude (degrees)
clat : latitude (degrees)
grossimx/y : zooming factor
in x/y
Computed as the ration of the
Finest model grid mesh length and of the equivalent length for the regular grid with same number of points.
dzoomx/y : fraction of the grid in which the resolution is increased.
taux/y : « stiffness »
http://lmdz.lmd.jussieu.fr/developpeurs/notes-techniques

---
Nudging
        Time constant for the relaxation of the model wind toward analyses
size 28 { { { partial u } over { partial t} = {{ partial u } over { partial t} } _{GCM} + { u_{analysis} - u} over { %tau } } }
Nudging :
Relaxation toward analyzed fields
size 28 { { { partial v } over { partial t} = {{ partial v } over { partial t} } _{GCM} + { v_{analysis} - v} over { %tau } } }
size 28 { { %tau }}
size 28 { { u_{analysis} v_{analysis} } }
ok_guide=y
guide_u= y
guide_v= y
guide_T= n
guide_P= n
guide_Q= n
tau_min_u=0.0208333
tau_max_u=10
tau_min_v=0.0208333
tau_max_v=10
Strong nudging
(t=30min)
Weaker nudging
(t=10 days)

---
size 20 { { P_1 ..... W_1=0 } }

---
size 28 { { P_{i,j,l} = A_l + Ps_{i,j} { } B_l } }
x1000
~/LMDZ/PEDAGO/VERT/vert.sh
~/LMDZ/NOTES/RESOLV/vertz.png

---
Time in seconds

---
Time in seconds

---
Time in seconds

---
Time in seconds

---
Time in seconds

---
Time in seconds

---
Contrôle du pas de temps dans gcm.def
day_step=960
## periode pour le pas Matsuno (en pas)
iperiod=5
Time in seconds

---
Controling the time-step in gcm.def
day_step=960
## period for the scheme Matsuno (in steps)
iperiod=5
Time in seconds

---
Example of dissipation computation in 1D on an initial field
consisting of the sum of two sign functions + a numerical mode

---
Controling dissipation in gcm.def
## dissipation periodicity (in time-step)
idissip=5
## Disssipation operator choice (star or non star )
lstardis=y
## number of iterations for the dissipation gradiv
nitergdiv=1
## number of iterations for the dissipation nxgradrot
nitergrot=2
## number of iterations for the dissipation divgrad
niterh=2
## dissipation time for the smallest wave length for u,v (gradiv)
tetagdiv=5400.
## dissipation time for the smallest wave length for u,v (nxgradrot)
tetagrot=5400.
## dissipation time for the smallest wave length for h ( divgrad)
tetatemp=5400.

---
Example of parameter tuning in gcm.def
Sensibility tests to horizontal resolution (Foujols et al.)
 http://forge.ipsl.jussieu.fr/igcmg/wiki/ResolutionIPSLCM4_v2

---
Large scale advection
Introduction of the Van Leer I scheme (1977), a second order finite volume scheme with slope limiters
(MUSCL, MINMOD) (Hourdin et Armengaud, 1999).
Guaranty of fundamental physical properties of transport :
conservation of the total quantity, postitivity, monotony, non increase of extrema, weak numerical diffusion
1D advection test with a Gaussian bell
        Initial distribution
        Exact solution (translation)‏
        Computation with advection scheme
U constant, CFL number U dt/dx = 0.2
U
Scheme I by Van Leer (1977)‏
c
size 12{ ital "ρvcδt"} {}
x
i-1
i
i+1
Centered finite differences (second order)‏
c
size 12{ ital "ρvc"} {}
x
i-1
i
i+1
Upwind first order scheme (Godunov, 1952)‏
c
size 12{ ital "ρvcδt"} {}
x
i
i-1
i+1
[Speaker Notes: Pour le transport grande échelle, j'ai introduit dans le modèle un schéma de transport en volume fini proposé à l'origine dans un très joli article par Van Leer 1977. Le schéma de Van Leer est intéressant parce qu'il permet de garantir un certain nombre de propriétés importantes du transport comme lire la liste. La présentation de ce schéma est très simple. Si on suppose qu'a un instant t, on une concentration ci dans la maille i, on va en fait plaquer sur la maille i une distribution sous-maille de traceur de moyenne ci et de pente calculée par différence finie avec les deux mailles voisines. On calcule ensuite le transfert de traceur entre la maille i et la maille i+1 au cours du pas de temps dt en multipliant le transfert de masse d'air entre les deux maille par la concentration moyenne de traceur dans l'air transferé. Tel quel, se schéma n'est pas positif. Mais, si on impose en plus que l'ensemble de cette distribution dans la maille i soit comprise entre les concentrations moyennes dans les deux mailles adjacentes, alors on obtient un schéma positif et monotone. Ce schéma peut etre vue comme une sophistication du schéma amont de Godunov, ou on suppose que la concentration ci est représentative de la concentration dans toute la maille i. Mais ce bon comportement physique est obtenu dans le schéma de Godunov au prix d'une diffusion numérique exagérée. Je montre ici un exemple d'advetcion uni-dimensionnelle d'un pic gaussien par un vent constant avec le schéma de Van Leer en bas, le schéma de Godunov au milieu et un schéma en différence finies centrées du deuxieme ordre. La solution exacte, en bleu, est simplement une translation de la distribution initiale en noire. On voit se créer des oscillations et des valeurs négatives avec le schéma centré. On voit le caractère très diffusif du schéma de Godunov et la meilleur conservation de la forme du pic par le schéma de Van Leer.]

---
dtvr = daysec / day_step
dtphys=iphysiq*dtvr
dtdiss=dissip_period*dtvr
dtvrtrac=iapp_trac*dtvr
Contraintes
dtvr limité par le CFL sur les ondes Cmax dt < min(dxmin,dymin)
dtrtrac limité par un CFL d'advection Umax dt < min(dxmin,dymin)
iphysiq, dissip_period,dtvrtrac = multiples de iperiod
iperiod (=5 par défaut) : fréquence d'appel à Matsuno
dtdiss << teta_temp, teta_rot, teta_temp
Grille régulière :
day_step(max(iim,jjm)=N) ~ day_step(max(iim,jjm)=M) * M/N
Grille régulière :
day_step (zoom) ~ day_step (reg) * max(grossismx,grossimy)

---
Main « calls » in dyn3d /leapfrog.F
CALL pression ( ip1jmp1, ap, bp, ps, p )
      CALL exner_hyb( ip1jmp1, ps, p,alpha,beta, pks, pk, pkf )
        call guide_main(itau,ucov,vcov,teta,q,masse,ps)
      CALL SCOPY( ijmllm ,vcov , 1, vcovm1 , 1 )
      CALL SCOPY( ijp1llm,ucov , 1, ucovm1 , 1 )
      CALL SCOPY( ijp1llm,teta , 1, tetam1 , 1 )
      CALL SCOPY( ijp1llm,masse, 1, massem1, 1 )
      CALL SCOPY( ip1jmp1, ps , 1, psm1 , 1 )
      CALL SCOPY ( ijp1llm, masse, 1, finvmaold, 1 )
      CALL filtreg ( finvmaold ,jjp1, llm, -2,2, .TRUE., 1 )
      CALL geopot ( ip1jmp1, teta , pk , pks, phis , phi )
      CALL caldyn
      CALL caladvtrac(q,pbaru,pbarv,
      CALL integrd ( 2,vcovm1,ucovm1,tetam1,psm1,massem1 ,
      CALL calfis( lafin , jD_cur, jH_cur,
      CALL top_bound( vcov,ucov,teta,masse,dufi,dvfi,dtetafi)
      CALL addfi( dtvr, leapf, forward ,
      CALL dissip(vcov,ucov,teta,p,dvdis,dudis,dtetadis)
      CALL dynredem1("restart.nc",0.0)
      CALL bilan_dyn(2,dtvr*iperiod,dtvr*day_step*periodav,
Physical tendencies U, q, q → F, Q, Sq
Time integration for physical tendencies
(U, q, q) t+dt = (U, q, q)t + dt * ( F, Q, Sq)

---
Main « calls » in dyn3d /leapfrog.F
CALL pression ( ip1jmp1, ap, bp, ps, p )
      CALL exner_hyb( ip1jmp1, ps, p,alpha,beta, pks, pk, pkf )
        call guide_main(itau,ucov,vcov,teta,q,masse,ps)
      CALL SCOPY( ijmllm ,vcov , 1, vcovm1 , 1 )
      CALL SCOPY( ijp1llm,ucov , 1, ucovm1 , 1 )
      CALL SCOPY( ijp1llm,teta , 1, tetam1 , 1 )
      CALL SCOPY( ijp1llm,masse, 1, massem1, 1 )
      CALL SCOPY( ip1jmp1, ps , 1, psm1 , 1 )
      CALL SCOPY ( ijp1llm, masse, 1, finvmaold, 1 )
      CALL filtreg ( finvmaold ,jjp1, llm, -2,2, .TRUE., 1 )
      CALL geopot ( ip1jmp1, teta , pk , pks, phis , phi )
      CALL caldyn
      CALL caladvtrac(q,pbaru,pbarv,
      CALL integrd ( 2,vcovm1,ucovm1,tetam1,psm1,massem1 ,
      CALL calfis( lafin , jD_cur, jH_cur,
      CALL top_bound( vcov,ucov,teta,masse,dufi,dvfi,dtetafi)
      CALL addfi( dtvr, leapf, forward ,
      CALL dissip(vcov,ucov,teta,p,dvdis,dudis,dtetadis)
      CALL dynredem1("restart.nc",0.0)
      CALL bilan_dyn(2,dtvr*iperiod,dtvr*day_step*periodav,
Computation of pressure from Al, Bl coefs
Nudging
Longitudinal filtering near poles
Hydrostatic equation vertical integration
Computation of dynamical tendencies
Tracer advection
Time integration for dynamics
Physical tendencies U, q, q → F, Q, Sq
Time integration for physical tendencies
(U, q, q) t+dt = (U, q, q)t + dt * ( F, Q, Sq)
Horizontal dissipation